## Slide 1: Reaching Impact, Saturation, and Epidemic Control (RISE): POCUS in COVID-19
Notes: May add the MOH logo if required/requested by host country government

## Slide 2: Learning Objectives
To learn the technique for performing pulmonary ultrasound.
To identify normal pulmonary ultrasound finding.
To identify the common pulmonary ultrasound findings in various pulmonary pathologies ( effusion, Pneumothorax, Acute Interstitial syndrome and pneumonia)
To identify the common pulmonary ultrasound findings in patient with COVID-19.

## Slide 3: Transducers

## Slide 4
Tansducer Type | Pros | Cons
Curvilinear | Ideal for Lung Ultrasound Good Combination of Resolution and Depth Large field of view to see multiple spaces | Large foot print can make it difficult to visualize through a single rib space. May need to switch for cardiac imaging Near field resolution may not be as optimal as with linear probe.
Phased Array | Deep penetration Small footprint to examine between single intercostal space Useful when also doing cardiac exam | Difficult to get precise definition of pleural line Near field resolution not as optimal as linear probe
Linear Probe | High resolution, resulting in precise definition of pleural line. Great for evaluating pleural line and subpleural consolidations | Due to the higher frequency, linear transducers are not ideal for visualizing structures past 6 cm Might miss pleural effusions and deep consolidations

## Slide 5: Lung Examination
Patient position: Usually Supine
Transducer Type:
  Linear: For superficial Structures
  Curvilinear: Deeper structures
Procedure
  Always examine both lungs.
  Probe is placed perpendicular on the chest wall with the pointer oriented cranially.
  Lawn mower technique

## Slide 6: Lung Examination Zones
Lung Zone 1/ L1
  2nd 3rd and 4th intercostal spaces, anterior chest wall.
Lung Zone 2/L2
  5th- 8th intercostal spaces, anterior chest wall
Lung Zone 3/L3
  4th -10th intercostal spaces between the anterior and posterior axillary lines.

## Slide 7: Lung Signs
Bat Sign/Normal
Transducer at L1, with the marker Cephalad
The sign is formed by shadows of two ribs and the pleural line (looks like a bat flying towards you)
  Try to obtain this image initially, to avoid artifacts

## Slide 9: Structures to be Identified
Skin
Subcutaneous tissue
Muscular layer
Ribs on either side (cortex with shadowing) with Intercostal layer in between
Pleura

## Slide 10: Lung Signs (Cont.)
Lung sliding (Normal)
  Movement of the Pleura with breathing will generate the “ Lung Sliding” sign
  Also called as the marching ant sign.

## Slide 11: Lung signs (cont.)
Lung Sliding (cont.)
  Lung sliding can sometimes be better evaluated with the M Mode generating the “Sea Shore” sign.
  The presence of the lung sliding and the sea shore sign, mostly rules out pneumothorax.

## Slide 12: Lung Signs (cont…)
A lines (Normal)
  Horizontal, echogenic reverberation artefacts that occur beneath the pleural line.
  Indicate dry interlobular septa
https://www.bcfultrasound.com

## Slide 13: Pathologies
Pleural effusion/hemothorax
Pneumothorax
Acute Interstitial Syndrome
Pneumonia

## Slide 14: Pleural Effusion/ Hemothorax
Patient Position
  Supine
Pulmonary regions
  Lung Zones L3, L4
Transducer Type and Placement
  Phased Array or curvilinear
  The footprint is perpendicular to the skin with the marker pointing cephalad

## Slide 15: Pleural Effusion/ Hemothorax
Start at the lower edge of Zone 3 and slide the transducer cephalad to detect the interface between the Diaphragm and Pleural space
Structures to be identified
  Chest wall
  Diaphragm
  Lung
  Pleural Effusion
  Liver or Spleen

## Slide 16: Pleural fluid assessment
THORACIC SPINE SIGN

## Slide 17: Quad Sign

## Slide 18: Sinusoidal Sign

## Slide 19: Pleural Effusion
Fluid Volume
  Measure the fluid depth at the lung base or the level of the 5th intercostal space
  Measurement starts 3 cms from the inferior pole of the lung to the chest wall
  >5cm fluid thickness indicates pleural effusion >500 ml

## Slide 20: Pneumothorax
CXR vs. USG
  PTx is misdiagnosed with CXR in 30-40% cases
  Half of radio-occult PTx yield tension PTx
  Bedside USG is more sensitive than CXR for diagnosis of PTx
    9 comparative trials
Lichtenstein et al. Crit Care Med 2005; 33:1231–1238 Rowan et al. Radiology 2002; 225:210 –214 Kirkpatrick et al. J Trauma2001; 50:750 –752

## Slide 21: Pneumothorax
Transducer Placement:
  Perpendicular to the skin, with marker pointing cranially in zones L1, L2 and L3
  Examine all zones while sliding the probe from one zone to another (Lawn Mower Technique)
Structures to be identified:
  Ribs, Intercostal area, Pleural, lungs.
  Bat sign

## Slide 22: Absent Lung Sliding Sign

## Slide 23: Lung Signs (cont.)
Absent Sliding
Can be absent in pneumothorax, atelectasis, pleurodesis, parietal emphysema or any cause that interrupts normal pleural movement

## Slide 24: Stratosphere Sign

## Slide 25: Pneumothorax
Lung Point
  A localized transition point from intrapleural air (Pneumothorax artifact) to intraparenchymal air- 100% specific for pneumothorax.
  The transition from Seashore sign to Stratosphere sign on the M-Mode

## Slide 26: Lung Point

## Slide 27: Curtain Sign

## Slide 28
Acute Interstitial Syndrome (AIS)

## Slide 29: Acute Interstitial Syndrome
Transducer Placement:
  Perpendicular to the skin, with marker pointing cranially in zones L1, L2 and L3
  Examine all zones while sliding the probe from one zone to another (Lawn Mower Technique)
Structures to be identified:
  Ribs, Intercostal area, Pleural, lungs.
  Bat sign

## Slide 30: Comet Tail Artifact/B-line
Laser Like vertical lines
Extending from the Pleural line upto the edge of screen without fading.
Synchronized with lung sliding
Overshadow the A lines.

## Slide 32: B-Line

## Slide 33: Pneumonia
Patient Position
  Supine
Pulmonary regions
  Lung Zones L3, L4
Transducer Type and Placement
  Phased Array or curvilinear
  The footprint is perpendicular to the skin with the marker pointing cephalad

## Slide 34: Pneumonia
Early pneumonia maybe seen as localized B-lines
Bacterial pneumonia typically displays ‘hepatization’ with increased consolidation. ( Tissue like sign)
Other visible signs:
  Air Bronchogram
  Shred Sign

## Slide 35: Summary
Assessment of a patient with Breathlessness

## Slide 36: Summary

## Slide 37
POCUS in COVID 19 pandemic

## Slide 40: Triage area
Normal scan
Abnormal scan
“A” profile
Pleural shredding
“B” profile
Quarantine
Shift to Emergency Department

## Slide 41: Lung ultrasound findings
Pleural line irregularities
Patchy sub-pleural consolidation
Tissue like patterns with static or dynamic air-bronchogram
Normal pleural line
Disrupted pleural lines

## Slide 42: Characteristic findings
Thickening of the pleural line with pleural line irregularity
B lines in a variety of patterns including focal, multifocal, and confluent
Consolidations in a variety of patterns including multifocal small, non-translobar, and translobar with occasional mobile air bronchograms
Appearance of A lines during recovery phase
Pleural effusions are uncommon

## Slide 44
BMJ-Postgraduate Medical Journal

## Slide 45
BMJ-Postgraduate Medical Journal

## Slide 46: Thank You!
This presentation was made possible with support from the United States Agency for International Development funded RISE program, under the terms of the cooperative agreement 7200AA19CA00003. The contents are the responsibility of the RISE program and do not necessarily reflect the views of USAID or the United States Government.​