## Slide 1: Mechanical Ventilation

## Slide 2: Learning Objectives
To understand the Basics of Respiration
Explore Indications and goals of Mechanical Ventilation
Be Familiar with normal parameters of Mechanical Ventilation
Overview Modes of Mechanical Ventilation
Discuss Complications of Mechanical Ventilation

## Slide 3: Respiratory Anatomy
Image: Wikimedia commons

## Slide 4: Respiratory Anatomy
Image: Wikimedia commons
Notes: Important to highlight the alveoli as the centers for gas exchange

## Slide 5: Mechanism Of Breathing
Brainstem Control
Chemo-receptors
Diaphragm contraction and chest wall expansion
Increased Intrathoracic Volume
Negative Intrathoracic Pressure
Air flows from high to low pressure
Negative pressure Ventilation

## Slide 6: Mechanism Of Breathing

## Slide 7: Introduction
Mechanical Ventilation is indicated when the patient’s spontaneous ventilation is inadequate to sustain life.
The ventilator delivers airs, usually with an elevated oxygen content, to a patients lungs via an endotracheal tube to facilitate the exchange of oxygen and carbon-dioxide.

## Slide 8: Goals and purpsoes
Improve gas exchange
Relive respiratory distress
Improve pulmonary mechanics
Permit lung and airway healing
Reverse hypoxemia
Relieve acute respiratory acidosis
Reverse respiratory muscle fatigue
Prevent and reverse atelectasis
Improve lung compliance
Mechanical ventilation alone does not treat or reverse the underlying
pathology

## Slide 9: Indications
Indications for Ventilatory Support
Airway Protection
Hypoxemic Respiratory Failure
Hypercapnic Respiratory Failure
Combination of both (Hypoxemia+ hypercapnia)
Cardiovascular Insufficiency (sepsis, shock, congestive heart failure)

## Slide 10: Respiratory Mechanics
Ventilation can occur only when sufficient pressure is applied to overcome two forces that oppose the movement of the respiratory system.
Elastic Forces (quantified as compliance)
Viscous Forces (quantified as resistance)
05

## Slide 11: Respiratory Mechanics
06

## Slide 12: Airway Pressure
Peak inspiratory pressure: The pressure used to deliver the tidal volume by overcoming nonelastic (airways) and elastic (lung parenchyma) resistance.
Plateau pressure: The pressure needed to maintain lung inflation in the absence of airflow.
07

## Slide 13: Static and Dynamic Pressure
Time
Pressure
PEEP
PIP
Pplat
Alveolar Distending (recoil)
Pressure difference (P distension)
Flow-Resistive
Pressure difference (P resistive)
08

## Slide 14: Compliance
Lung compliance is volume change (lung expansion) per unit pressure change (work of breathing), and it is calculated by C = DV/DP
10
When lung compliance is decreased (eg. atelectesis), both plateau pressure (Pplat) & peak pressure (PIP) are increased.

## Slide 15: Compliance
When airway resistance is increased (eg. bronchospasm), PIP is increased but Pplat remains unchanged.
20
11

## Slide 16: Compliance
Clinical Conditions that decrease the Compliance | 
Type of Compliance | Clinical Conditions
Static Compliance | ARDS Atelectasis Tension Pneumothorax Obesity Retained secretions
Dynamic Compliance | Bronchospasm Kinking of ET tube Airway onbstruction

## Slide 17: Invasive Positive Pressure Ventilation
Full ventilatory support: the ventilator provides all the energy necessary to maintain effective alveolar ventilation
Partial ventilatory support: the ventilator provides partial support and the patient participates in work of breathing to help maintain effective alveolar ventilation
15

## Slide 18: Types of Breath Delivery
Controlled
  Ventilator controls the timing, tidal volume or both
Spontaneous
  Patient controls the timing and the tidal volume
Assisted
  Characteristics of both spontaneous and mandatory breaths
  All or part of the breath is generated by the ventilator
  The patient triggers and cycles the breath
16

## Slide 19: Control Variables
VOLUME PRESET
  Set parameter is the tidal volume; airway pressure is variable
  Constant tidal volume in the face of changing lung characteristics
  Fixed flow rate: Insufficient flow may give rise to Patient-ventilator dyssynchrony.
PRESSURE PRESET
  Set parameter is airway pressure; tidal volume delivered is variable
  Tidal volume varies with changes in lung characteristics
  Flow will vary according to patient's demands

## Slide 20: Key Elements of conventional modes
time
Pressure
PEEP
PIP
Pplat
Trigger
Limit
Cycle
18

## Slide 21: Key elements of Conventional Modes
Trigger (Start) - Machine initiated ( Time), Patient initiated (Volume/ Flow)
Limit (Target) – Volume, Pressure, Flow
Cycle (Stop)- Time, Volume, Flow, Pressure
19

## Slide 22: Vent Terminology

## Slide 23: Vent Terminology

## Slide 24: Ventilatory Settings
Tidal Volume
PEEP
Mode (type of assist given by ventilator)
Rate (breaths per minute adjusted based on patients own respiratory rate)
FiO2 (amount of O2 being delivered)

## Slide 25: PEEP (Positive End Expiratory Pressure)
Pressure given in expiratory phase to prevent closure of the alveoli and allow increased time for O2 exchange.
Used in patients who haven’t responded to treatment and are requiring high amount of FiO2.
PEEP will lower O2 requirement by recruiting more alveoli.
Normal PEEP is approximately 5cmH2O, can be as high as 20cmH2O.

## Slide 26: Modes of Mechanical Ventilation
CMV – Continuous Mandatory Ventilation : PC/VC
ACV - Assist Control Ventilation : PC/VC
SIMV - Synchronised Intermittent Mandatory Ventilation: PC/VC
PSV – Pressure Support Ventilation
APRV- Airway Pressure Release Ventilation
20

## Slide 27: Controlled Mechanical Ventilation
In this mode the ventilator provides a mechanical breath on a pre-set timing.
Patient respiratory efforts are ignored.
This is generally uncomfortable for children and adults who are conscious and is usually only used in an unconscious patient

## Slide 28: Assist Control Mechanical Ventilation
Most frequently mode used in Intensive care unit.
Tidal Volume and rate are preset and guaranteed, ensuring minimum minute ventilation.
Patient can trigger additional machine assisted breaths above set rate.
Machine delivers the same tidal volume during every inspiration, whether initiated by ventilator or patient.

## Slide 29: Assist Control Mechanical Ventilation
The work of breathing is reduced to amount of inspiration needed to trigger inspiratory cycle of machine.

## Slide 30: Synchronized Intermittent Mandatory Ventilation (SIMV)
Pre-set mechanical breath (pressure or volume limited)
  Respiratory rate of 12 results in a 5 second cycle time.
Within that cycle time the ventilator waits for the patient to initiate a breath using either a pressure or flow sensor.
When the ventilator senses the first patient breathing attempt within the cycle, it delivers the preset ventilator breath.

## Slide 31: Synchronized Intermittent Mandatory Ventilation (SIMV)
If the patient fails to initiate a breath, the ventilator delivers a mechanical breath at the end of the breath cycle.
Additional spontaneous breaths after the first one within the breath cycle do not trigger another SIMV breath.
Weaning mode

## Slide 32: Synchronized Intermittent Mandatory Ventilation (SIMV)

## Slide 33: Pressure Support Ventilation
Spontaneous mode
Patient initiates breath and ventilator delivers pre-set inspiratory pressure to help overcome airway resistance
Patient controls the rate, tidal volume and minute ventilation
TV is variable
Can be used in conjunction with SIMV or CPAP
ALWAYS set low TV / MV alarm and apnea backup

## Slide 34: Airway Pressure Release Ventilation (APRV)
Differs from conventional Vent
Elevation of airway pressures with brief intermittent release of airway pressure.
Facilitates oxygenation and CO2 clearance.
Maybe an deployed in ALI/ARDS.

## Slide 35: Complications of Mechanical Ventilation
Asynchrony (“bucking”)
Auto PEEP
  Patient does not expire full tidal volume and air becomes trapped.
  Can cause increased alveolar damage.
Baro-Trauma
  Damage to alveoli caused by increased pressure and volume.

## Slide 36: Complications of Mechanical Ventilation
Hemodynamic Compromise
Nosocomial infection
Ulcers/gastritis/malnutrition
Muscle deconditioning/ Vent dependence

## Slide 37: Thank You